## Slide 1: Environmental Health and Safety Hazardous Waste Training

## Slide 2
“Why do we have to take this class?”
It’s the Law and for your safety!
“How often do I take this training?”
Annually

## Slide 3
Hazardous Waste training is an ANNUAL requirement. Please plan on attending this training again or take the online refresher within one year of today’s date if you are still working in a lab and may be handling hazardous waste.
Training options:
  Training class
  Online refresher https://sc.edu/about/offices_and_divisions/ehs/index.php

## Slide 4
Items covered in this training:
Regulations for Hazardous Waste
What is a Waste?
        Making a Waste Determination / Universal Waste / Non-Regulated Waste
Satellite Accumulation Area Requirements
Waste Management in the Labs
Spills – Who is responsible and what to do
Waste Pick-up Procedure
What happens when my lab is not compliant?
Quiz

## Slide 5
Regulation of Hazardous Waste
Who Regulates the University?
  RCRA- Resource Conservation and Recovery Act (overseen by EPA) is the public law that creates the framework for the proper management of hazardous and non-hazardous solid waste. The law describes the waste management program mandated by Congress that gave EPA authority to develop the RCRA program. Enacted in 1976.
EPA - Environmental Protection Agency (est. 1970)
  Born in the wake of elevated concern about environmental pollution, EPA was established to consolidate in one agency a variety of federal research, monitoring, standard-setting and enforcement activities to ensure environmental protection. Since its inception, EPA has been working for a cleaner, healthier environment for the American people
Notes: I just make a point to state that DHEC will often inspect use but report the findings to the EPA
DOT-Many chemicals may not meet the definition of HW but are regulated for transport. I usually point out that if they receive a chemical with a warning label then they at least have a DOT hazardous material and it will likely have to collect it all the same.

## Slide 6
Regulations for Hazardous Waste (cont.)
Who Regulates the University?
SCDHEC- is charged with upholding the requirements in the Solid Waste Policy and Management Act, meaning that at least once every five years, the DHEC shall review each permitted facility. They inspect facilities and files. They enforce compliance for the best interest of the health of the people and the environment of SC.
D.O.T. – Department of Transportation is a cabinet-level agency of the federal government responsible for helping maintain and develop the nation’s transportation systems and infrastructure. From roads to airlines to railways, DOT carries out planning that supports the movement of Americans by cars, truck, trains, ships and planes.
Notes: I just make a point to state that DHEC will often inspect use but report the findings to the EPA
DOT-Many chemicals may not meet the definition of HW but are regulated for transport. I usually point out that if they receive a chemical with a warning label then they at least have a DOT hazardous material and it will likely have to collect it all the same.

## Slide 7
What is a Waste?
A waste is ANY solid, liquid or contained gaseous material that:
  Is beyond it’s expiration date
  OR
  Is no longer viable for it’s intended purpose and is to be discarded

## Slide 8
What is a Hazardous Waste?
Listed Hazardous Waste
  D-Listed – Waste that has a hazardous characteristic
  F-listed – Non-specific source wastes (Ex. - Spent solvents)
  K-listed – Specific-source wastes (Generally not generated by the University)
  P-listed & U-listed – Unused Commercial Chemical Products
Special Exception for P-Listed Chemicals: Empty containers that held p-listed chemicals must be tagged and disposed of as a hazardous waste!

## Slide 9
What is a Hazardous Waste? (cont.)
Characteristic Hazardous Waste (D-Listed)
  Ignitable (D001) – Ignitable wastes include oxidizers and liquid, solids and gases that have a flashpoint of <140 °F
Corrosive (D002) – pH  2 (acidic) or pH  12.5 (basic)
Reactive (D003) – Water or air reactive waste that produces toxic fumes
Toxic (D004-D043) – Materials that potentially threaten human and/or wildlife health

## Slide 10
What is a Hazardous Waste? (cont.)

## Slide 11
Universal Waste and Non-regulated Waste
Universal Waste –
Includes all mercury containing devices.
Must be tagged and disposed of through the USC HW Program as Universal Waste
Broken devices must be cleaned up immediately, tagged and disposed of as hazardous waste
Non-Regulated Waste – May be disposed of in regular trash
Empty containers
Broken glass
Non-contaminated PPE and glassware

## Slide 12
Waste Management in Satellite Accumulation Areas (SAA) (i.e. – Laboratories)
Requirements for SAA’s
      Waste container must be at or near the point of generation of the waste
      Waste container must be properly labeled
      Waste container must be closed at all times except for when adding waste
      No more than 55 gallons of waste may be stored at any time.
      Waste determination must be made a point of generation.

## Slide 13
Container Types
Container must be compatible with contents
Containers must be capable of closing
  No corks, stoppers, foil, or parafilm
No glass containers
Completely deface all old labels if reusing containers
USC EH&S provides HDPE 10L carboys, 4L, 1000mL, 500mL, and 5-gallon buckets

## Slide 15
Making a Hazardous Waste Determination
  The waste determination must be made at the point of generation (i.e. – Lab or shop)
  All chemical constituents and amounts (%, ppm, mL) must be known and included on the USC waste tag
  All chemical hazards must be known and included on the waste tag
  Check Safety Data Sheets (SDS) for chemical hazards and compatibilities
  HAZARDOUS WASTE MAY NOT BE DILUTED TO RENDER IT NON-HAZARDOUS

## Slide 16
Hazardous Waste Container Labeling
All hazardous waste containers must be labeled with the following:
  The words “Hazardous Waste”
  All chemical constituents (Only technical names. No chemical formulas (C3H6O) or trade names. This is the USC waste tag provided by USC EH&S.
  Indicate all chemical hazards of the waste in the container

## Slide 17
USC Pre-printed Waste Labels

## Slide 18
Off-Spec Waste / Rejected Waste
Off-spec waste will not be picked up
ex. Unlabeled container
Glass container
Incorrect constituents
Missing information
A rejection sticker will be placed on any off-spec container and the container will be left in the lab. Email the HW Manager once the issue has been corrected and your container will be picked up.

## Slide 19
What’s wrong?
Hint, look at obvious

## Slide 20
What’s wrong?
What makes it acidic?
Does it equal 100%?

## Slide 21
What’s wrong?
Hint, look at obvious

## Slide 22
What’s wrong?
Abbreviations DO NOT DO IT!!
What is “AA waste and ICP waste”
Who does this belong to?
Building?
Totals?
What makes it Acidic?

## Slide 23
Chemical Spills / Housekeeping
Ensure that all waste is handled cautiously
The laboratory is responsible for cleaning up all spills
Spills must be cleaned up immediately
Spilled materials that are contaminated with hazardous waste must be handled as hazardous waste Ex. - Gloves, towels absorbent material, etc.
It is not the responsibility of custodial staff to clean up chemical spills!!

## Slide 25
Waste Pick-up Procedures
Requests must be made through the USC Hazardous Waste Database
The database can be found at:
https://sc.edu/about/offices_and_divisions/ehs/index.php
Waste pick-ups are every Wednesday
Requests must be made before noon on the Tuesday prior for the waste to be picked up the following day

## Slide 30
Fill form out for each container.
Each container must have its own tag.
EH&S track each container from “Cradle to grave”

## Slide 31
Waste Minimization
Do not mix hazardous and non-hazardous waste
Do not buy chemicals in bulk, when possible

## Slide 32
Consequences of Regulatory Non-compliances
If your lab is cited for regulatory non-compliances that result in a monetary fine, your Department is responsible for paying the civil penalty
Civil penalties can result in up to $25,000 per violation per day.

## Slide 33
HW Competency Quiz and Certificate
In order to obtain your certificate for this class you must take the HW quiz online located on the EHS website.
https://sc.edu/about/offices_and_divisions/ehs/index.php
20 Questions
  80% or greater is a passing grade
  Certificate will be available to print immediately
  Ensure a copy of your training certificate is placed in your lab’s Chemical Hygiene Plan

## Slide 34
In Case of Emergency
Campus Emergency Number 777-9111
EH&S 777-5269
Chemical Spills – Call EH&S 777-5269
Ensure your lab has a fire extinguisher
If bodily injury occurs, call 777-9111 immediately or go to Thompson Student Health Center

## Slide 35
Please visit the USC EH&S website @
https://sc.edu/about/offices_and_divisions/ehs/index.php
If you have any questions or need any additional information, please contact:
Jeff Brannon – USC Hazardous Waste Manager
University of South Carolina
EHS Office
226 Bull St., Office 301-E
brannonm@mailbox.sc.edu
(803)777-1935

## Slide 36
Thank you and be safe!!!!